## Slide 1: Computer Architecture
System Software Crash Course

## Slide 2: Agenda
Computer architecture
CPU Architecture

## Slide 3: Computer Architecture

## Slide 4: Computers in Our Life

## Slide 5: Computer Organization

## Slide 6: Instruction Set Architecture
The words of a computer’s language are called instructions, and its vocabulary is called Instruction Set.
The Instruction Set Architecture is a abstract model of computer, it serves as the interface between software and hardware.
The ISA is based on idea of stored program: instructions and data can be stored in memory as numbers.
The goal for ISA design: find a language that makes it easy to build hardware and compiler while maximizing performance and minimizing cost and energy consumption.
In general ISA defines supported data types, state (main memory, registers), instructions and input/output model.

## Slide 7: Instruction Set Architecture
Arithmetic and logic instructions:
  Add, subtract, multiply, divide, increment, decrement;
  Bitwise operations: bitwise and, bitwise or, bitwise exclusive or, negation, shifts;
  Comparison: equal, not equal, less, greater, less or equal, greater or equal, comparison to zero;
  Floating-point arithmetic and comparison.
Data handling:
  Copy data to or from register or memory (also loading and storing);
  Set a register to fixed value;
  Read or write hardware device.
Control flow:
  Jump to another program location;
  Conditionally branch to another location;
  Indirectly branch to another location;
  Call another procedure saving next instruction pointer.

## Slide 8: Addressing Modes
An addressing mode specifies how to calculate the effective memory address of an operand by using information contained within a machine instruction
Addressing modes for code:
  Sequential execution: EA = next instruction address
  Absolute or direct: EA is address parameter itself
  PC-relative: EA = next instruction address + offset parameter
  Register indirect: EA = contents of a register

## Slide 9: Addressing Modes
Addressing modes for data:
  Implicit: implied by operation code
  Immediate: value of operand is held within instruction itself
  Register: value is held in a register
  Absolute or direct: EA is an address parameter
  Based: EA = content of a register + value of immediate operand
  Register indirect: EA = contents of a register
  Based with index: EA = contents of base register + contents of index register + value of immediate operand
  Scaled: EA = contents of a register * scale + value of immediate operand
  Autoincrement: EA = content of a register; register is incremented

## Slide 10: Von Neumann Architecture
Von Neumann architecture is based on stored program concept.
Allows program tooling: programs that write programs.
Von Neumann bottleneck: limited throughput between CPU and memory.

## Slide 11: Harvard
Harvard architecture physically separates data and instruction memory.
Overcome von Neumann bottleneck
Increased cost of hardware

## Slide 12: Data Flow
Dataflow architectures do not have a program counter, the executability and execution of instructions is solely determined based on the availability of input arguments to the instructions

## Slide 13: CPU Architecture

## Slide 14: Central Processing Unit
Fetch
Decode
Control
Registers
Memory
PC
Write
ALU

## Slide 15: CPU Cycle
Fetch
Decode
Control
Registers
Memory
PC
Write
ALU

## Slide 16: CPU Cycle
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
LOAD | Fetch | Decode | Execute | Memory | Write |  |  |  |  |  | 
LOAD |  |  |  |  |  | Fetch | Decode | Execute | Memory | Write | 
ADD |  |  |  |  |  |  |  |  |  |  | Fetch

## Slide 17: Pipeline
 | 1 | 2 | 3 | 4 | 5 | 6 | 7
LOAD | Fetch | Decode | Execute | Memory | Write |  | 
LOAD |  | Fetch | Decode | Execute | Memory | Write | 
ADD |  |  | Fetch | Decode | Execute | Memory | Write

## Slide 18: Pipelined Central Processing Unit
Fetch
Decode
Control
Registers
Memory
PC
Write
ALU

## Slide 19: Reduced Instruction Set Computer
Pipelined execution unit.
Load/store based ISA: operations only on registers.
Simple addressing modes.
Large register file.
Three-operands instructions.
Separated instruction and data caches.

## Slide 20: Pipeline Advantages & Hazards
Advantages
  Asymptotic performance 1 operation per cycle
  Reduced hardware complexity
Hazards
  Structural hazards
  Data hazards
  Control hazards

## Slide 21: Structural Hazards
Planned instruction cannot execute because the hardware does not support the combination of instructions.
 | 1 | 2 | 3 | 4 | 5 | 6 | 7
LOAD | Fetch | Decode | Execute | Memory | Write |  | 
LOAD |  | Fetch | Decode | Execute | Memory | Write | 
ADD |  |  | Fetch | Decode | Execute | Memory | Write
STORE |  |  |  |  | Fetch | Decode | Execute

## Slide 22: Data Hazards
Pipeline must be stalled because one step must wait another to complete
 | 1 | 2 | 3 | 4 | 5
ADD R0, R1, R2 | Fetch | Decode | Execute | Write | 
SUB R3, R0, R4 |  | Fetch | Decode | Execute | Write
 | 1 | 2 | 3 | 4 | 5 | 6 | 7
LOAD R0, R1(20) | Fetch | Decode | Execute | Memory | Write |  | 
SUB R3, R0, R4 |  | Fetch | Decode | Stall | Stall | Execute | Write

## Slide 23: Control Hazards
The control hazard arises when CPU needs to make decision based on the result of one instruction while executing others
 | 1 | 2 | 3 | 4 | 5 | 6 | 7
ADD R4, R5, R6 | Fetch | Decode | Execute | Memory | Write |  | 
BEQ R4, R2, 40 |  | Fetch | Decode | Execute | Memory | Write | 
LOAD R3, 30(R0) |  |  | Fetch | Decode | Execute | Memory | Write
 | 1 | 2 | 3 | 4 | 5 | 6 | 7
ADD R4, R5, R6 | Fetch | Decode | Execute | Memory | Write |  | 
BEQ R4, R2, 40 |  | Fetch | Decode | Execute | Memory | Write | 
OR R7, R8, R9 |  |  | Stall | Stall | Stall | Fetch | Decode

## Slide 24: Forwarding
Stalling on data hazards reduces performance of CPU.
Forwarding: delivering result of a later pipeline stage to earlier one.
Increase complexity of the hardware:
  One need data dependency detection logic
  One need data forwarding logic
Compiler should re-arrange instructions to achieve maximal performance

## Slide 25: Branch Prediction
Control hazards handling strategies:
  Assume branch not taken
  Reduce the delay of branches
  Likely / unlikely branch instructions
  Dynamic branch prediction
Predict taken
Predict taken
Predict not taken
Predict not taken
Not Taken
Not Taken
Not Taken
Not Taken
Taken
Taken
Taken
Taken

## Slide 26: Thank you!